## Slide 1
AI-Based Adaptive Oil Spill Source Reconstruction Using Multi-Temporal Satellite Observations and Environmental Uncertainty
Review 2 Presentation
FACULTY GUIDE
Dr. Banu Priya Prathaban
Department of Computer Science & Engineering SRM Institute of Science and Technology
TEAM MEMBERS (NAMES & REG NOS)
• Jayalakshmi T (RA2411031010115) — Proposed Model Dev
• Sachin P (RA2411031010117) — Data Engineering
• Shivaani M (RA2411031010119) — Comparative Analysis
• Varsha U (RA2411031010120) — Visualization & Dashboard

## Slide 2
REVIEW 2 PRESENTATION STRUCTURE
Contents / Agenda
1. Dataset (Synthetic v4 Big Data & Sanchi Real Disaster Archives)
2. Proposed Model (Adaptive Spatial-Temporal ConvLSTM with Attention)
3. Overall System Architecture Diagram (Layer 1 to Layer 5 Workflow)
4. Preprocessing: Big Data Analysis & Pipeline Steps
5. Results of Preprocessing (Inserted Quantitative Table & Visual Dashboard)
6. Classification: Novel Proposed Classifier (AST-CLAM Architecture)
7. Results of Classification Using Proposed Model (Accuracy, F1, RMSE)
8. Comparison with Existing Classifier Models (RF, XGB, MLP, ConvLSTM, U-Net)
9. Plan of Action / Member Tasks Breakdown
10. References (Key High-Impact Literature Citations)
11. Attach Geotagged Photo Taken During Review 2 Presentation
12. Attach Google Colab Implementation Link

## Slide 3
DATA ENGINEERING
1. Dataset Specifications & Big Data Inventory
Comprehensive Big Data Table (v4 Full)
• 60,539,017 candidate grid rows across 5 whole-spill folds. • Stored in Apache Parquet (115 partitions, 2.39 GB on disk). • 1,000 synthetic spills under realistic 2018 East China Sea conditions. • Positive class ratio: 0.77% (cell <= 10 km and release <= 3 h).
Stratified Training Table (v4 Sample)
• 3,467,398 rows across 645 partitions (238.2 MB). • Retains 100% true positives + exactly 5% hash-sampled negatives. • Balanced sample weights (w_sample_weight) correct for negative sampling. • Partitions strictly split train/test by id_fold (zero spill leakage).
Real-World Sanchi Disaster Event Archive
• 20,951 candidate cells from Sentinel-1 SAR and VIIRS observations. • 632 audited tanker drift timestamps with AIS velocity alignment. • Benchmarked against verified wreck location at 115 m depth (28.375°N, 125.942°E). • 2 distinct satellite slicks captured on 18 Jan 2018.
Multi-Source Environmental Reanalysis Forcing
• ERA5 Atmospheric Reanalysis: Hourly 10m wind fields (u10, v10) at 0.25°. • CMEMS Physical Ocean Reanalysis: Surface current velocities (u, v) at 0.083°. • Stokes drift wave radiation stress and windage coefficient (3%). • Dynamic hourly forcing uncertainty wandering around drawn mean.

## Slide 4
NOVEL DEEP LEARNING ARCHITECTURE
2. Proposed Novel Deep Learning Model (AST-CLAM)
AST-CLAM: Adaptive Spatial-Temporal Convolutional LSTM with Attention Mechanisms
A physics-informed deep learning architecture designed to overcome environmental forcing divergence in satellite oil spill source reconstruction.
1. Tri-Branch Dynamic Decoupling
• Spatial Branch (14 dims): Encodes slick polygon centroid, particle dispersion radius, and cluster spread. • Environmental Branch (10 dims): Embeds ERA5 wind vectors, CMEMS currents, and 3% windage advection. • Drift Mismatch Branch (5 dims): Explicitly isolates advective trajectory divergence vectors (f_drift_err).
2. Adaptive Uncertainty Attention (AEU-Attn)
• Calculates dynamic cross-attention between spatial candidate states (Q) and environmental forcing uncertainty (K, V). • When drift mismatch indicates high sea-state turbulence, the attention gate downweights noisy advection. • Amplifies multi-snapshot consensus to preserve trajectory integrity.
3. Dual-Task Multi-Objective Heads
• Classification Head: Outputs source probability P(y_is_source=1) optimized via Focal Cross-Entropy Loss (alpha=0.75, gamma=2.0). • Centroid Offset Regression Head: Predicts continuous Euclidean distance offset (km) trained with Smooth L1 Huber Loss. • Ensures latent space is physically consistent with spatial coordinates.

## Slide 5
SYSTEM ENGINEERING WORKFLOW
3. Overall System Architecture & Data Pipeline
Layer 1: Ingestion
Sentinel-1 SAR Slicks ERA5 Wind (u10, v10) CMEMS Ocean Currents Sanchi Audited AIS Tracks
Layer 2: Big Data Preproc
PyArrow Distributed Engine Noise Cleaning & Scaling Physical Grid Imputation Adaptive Thresholding
Layer 3: Tri-Branch Fusion
Spatial Geometry (14 dims) Hydrodynamic Field (10 dims) Drift Mismatches (5 dims) Concatenation & Norm
Layer 4: AST-CLAM Core
Spatio-Temporal Conv1D Bidirectional LSTM Core AEU-Attn Uncertainty Gating Dual Classification/Offset
Layer 5: Decision Output
Calibrated Source Map Sub-10km Centroid RMSE Origin Localization Hit Real Wreck Recovery

## Slide 6
DATA ENGINEERING
4. Preprocessing: Big Data Analysis & Pipeline Steps
Step 1: Partitioned Big Data Extraction & Profiling
• Scanned and profiled full dataset archives (60.5M records) and representative sample folds. • Utilized Apache PyArrow Parquet engine to read Hive-partitioned files (Fold 0: 659,295 cells in 0.65s). • Enforced strict whole-spill partitioning by id_fold (0..4) to guarantee zero data leakage.
Step 2: Systematic Noise Cleaning & Outlier Suppression
• Identified physical anomalies and corrupted boundary values across spatial-temporal grid coordinates. • Handled drift ratio singularities (division by near-zero displacement) clipped to nominal [0.0, 10.0]. • Synchronized UTC time stamps across satellite observation frames and hourly ERA5 reanalysis.
Step 3: Physical Grid Parameter Imputation
• f_rank_in_hour (120,466 nulls): Missing when snapshot k has 0 particles in that grid cell. Physically imputed with 999.0 (unranked / zero-priority candidate). • f_drift_err (132,577 nulls): Missing for k=1 (single snapshot). Imputed with neutral baseline (0.0 km east/north mismatch, 1.0 nominal ratio).
Step 4: Adaptive Spatial-Temporal Thresholding & Feature Engineering
• Engineered 5 hydrodynamic interaction features: total forcing velocity, multi-snapshot consensus ratio, wind alignment. • Implemented dynamic quantile adaptive thresholding (80th percentile) combining particle share with Euclidean proximity, filtering 80% empty ocean background.

## Slide 7
DATA ENGINEERING
5. Results of Preprocessing: Quantitative Metrics Table
Preprocessing Parameter / Metric | Value | Operational / Physical Interpretation
Total Processed Records (Fold 0) | 659,295 | Hive-partitioned Parquet (200 Spills)
Ground Truth Source Positives (y=1) | 91,561 (13.89%) | Cell <= 10 km from source, release <= 3 h
Candidate Negatives (y=0) | 567,734 (86.11%) | Background ocean grid cells
Missing Grid Parameters Handled | 518,197 cells | 100% resolved without synthetic data drop
Missing f_rank_in_hour Imputed | 120,466 cells | Physical rank 999.0 (Unranked cell)
Missing k=1 Drift Mismatch Imputed | 132,577 cells | 0.0 km east/north, 1.0 nominal ratio
Engineered Interaction Features | 5 Features Added | Windage speed, consensus ratio, alignment
Adaptive Segmentation Threshold | 0.1448 | 80th percentile dynamic confidence
Segmented High-Potential Cells | 131,859 cells | Candidate region for deep learning
End-to-End Preprocessing Runtime | 1.48 s | High-throughput PyArrow execution

## Slide 8
DATA ENGINEERING
5. Results of Preprocessing: Visual Analytics Dashboard
Dashboard Insights:
Panel (A): Shows 100% resolution of missing rank and drift values.
Panel (B): ERA5 wind speed (mean ~6.8 m/s) and CMEMS current speed (mean ~0.22 m/s) distributions.
Panel (C): Clear bimodal separation of particle consensus between true source and background.
Panel (D): Dispersion across ensemble levels confirms 10km source radius bounding.

## Slide 9
NOVEL DEEP LEARNING ARCHITECTURE
6. Classification: Novel Proposed Classifier (AST-CLAM)
Feature Input Formulation (29 Dimensions)
• Spatial Geometry (14 features): f_dist_slick_km, f_dist_cloud_km, f_share_mean_1k, f_cloud_spread_km, etc. • Hydrodynamic Forcing (10 features): f_wind_speed_ms, f_current_speed_ms, fe_total_forcing_speed, fe_wind_alignment. • Drift Residuals (5 features): f_drift_err_east_km, f_drift_err_north_km, f_drift_ratio, fe_has_drift_vector.
Spatio-Temporal Sequence Modeling
• Spatio-Temporal Conv1D: Multi-channel 1D convolutions extract local candidate cell interactions. • Bidirectional Temporal LSTM: 2-layer BiLSTM captures retrograde temporal sequence dynamics (t = 0 to -120 h). • Models physical trajectory momentum and non-linear advective transport.
Adaptive Environmental Uncertainty Attention (AEU-Attn)
• Query (Q): Spatio-temporal candidate trajectory hidden state. • Key (K) & Value (V): Dynamic environmental forcing vectors & drift error residuals. • Formula: Context = Softmax(Q K^T / sqrt(d_k)) * V * UncertaintyGate(env_context). • Attenuates erroneous drift trajectories under turbulent sea states; amplifies multi-snapshot consensus.
Dual-Task Optimization Objective
• Total Loss = L_Focal + lambda * L_Huber • L_Focal = -alpha * (1 - p_t)^gamma * log(p_t) [alpha=0.75, gamma=2.0, combats 1:100 imbalance]. • L_Huber: Smooth L1 distance error regression on continuous source distance (km). • Forces latent embeddings to obey physical spatial Euclidean geometry.

## Slide 10
EVALUATION & METRIC VERIFICATION
7. Results of Classification: Proposed AST-CLAM Performance
ACCURACY
94.88%
+5.35% higher than best baseline
PRECISION
85.26%
Low false alarm candidate rate
RECALL
64.53%
Captures true source cells reliably
F1-SCORE
0.7346
+0.2457 higher than Random Forest
AUC-ROC
0.9870
Near-perfect ranking capability
CENTROID RMSE
6.86 km
Sub-10km operational requirement met

## Slide 11
COMPARATIVE ANALYSIS
8. Benchmark Comparison with 5 Existing Classifier Models
Model | Category | Accuracy | Precision | Recall | F1-Score | AUC-ROC | Centroid RMSE | Sanchi Wreck Err
Random Forest | Ensemble Bagging | 89.53% | 52.68% | 45.61% | 0.4889 | 0.8969 | 29.84 km | 25.79 km
XGBoost | Gradient Boosted Trees | 89.26% | 52.54% | 21.80% | 0.3081 | 0.8532 | 33.69 km | 33.13 km
Deep MLP | Feedforward DNN | 88.65% | 47.29% | 29.54% | 0.3637 | 0.8145 | 35.21 km | 58.69 km
Standard ConvLSTM | Spatio-Temporal Net | 89.06% | 50.62% | 12.07% | 0.1949 | 0.7841 | 30.79 km | 50.97 km
Attention U-Net | Chen & Wang (2022) | 88.64% | 43.90% | 12.52% | 0.1948 | 0.7828 | 29.86 km | 37.48 km
Proposed AST-CLAM | Novel Adaptive Attention | 94.88% | 85.26% | 64.53% | 0.7346 | 0.9870 | 6.86 km | 4.62 km
★ Benchmark Conclusion: Proposed AST-CLAM decisively outperforms all 5 baseline models across every quantitative metric and reduces Sanchi wreck localization error from 29.10 km (naive) to 4.62 km (84.1% distance reduction).

## Slide 12
COMPARATIVE ANALYSIS
8. Benchmark Comparison: Visual Evaluation Dashboard
Visual Findings:
Panel (A) ROC Curves: AST-CLAM curve dominates the top-left quadrant (AUC = 0.9870).
Panel (B) PR Curves: Sustained high precision across recall levels (Average Precision = 0.812).
Panel (C) Grouped Bar Chart: AST-CLAM leads across Accuracy, Precision, Recall, and F1.
Panel (D) Centroid Trajectory RMSE: AST-CLAM achieves 6.86 km (red bar), well below the 10km target threshold.

## Slide 13
PROJECT MANAGEMENT
9. Plan of Action & Team Member Task Progress
Member Name & Reg No | Responsibility Domain | Key Technical Contributions Executed | Status | 
Sachin P (RA2411031010117) | Data Engineering | Big Data ingestion (60.5M rows), Parquet partitioning, missing parameter physical imputation, adaptive thresholding | Completed (Review 2) | 
Shivaani M (RA2411031010119) | Comparative Model Analysis | Benchmark evaluation of RF, XGBoost, Deep MLP, Standard ConvLSTM, Attention U-Net against AST-CLAM | Completed (Review 2) | 
Jayalakshmi T (RA2411031010115) | Proposed Model Development | Novel AST-CLAM architecture design, AEU-Attention module, Dual-Task Focal + Huber distance loss optimization | Completed (Review 2) | 
Varsha U (RA2411031010120) | Visualization & Dashboard | Interactive Power BI spatial trajectory dashboard, hydrodynamic wind/current overlay, web UI deployment | In Progress (PBL 3 Final) | 
ℹ Evaluator Directive: Review 2 focuses on Big Data preprocessing, novel deep learning architecture, and 5-model comparative benchmarking. Interactive visualization dashboard will be presented in PBL Review 3.

## Slide 14
REFERENCES
10. Key References (Literature Benchmark)
[1] S. El Mohtar et al., 'Bayesian identification of oil spill source parameters from image contours,' Marine Pollution Bulletin, vol. 169, Art. no. 112514, 2021.
[2] M. A. E. R. Hammoud et al., 'Moving source identification in an uncertain marine flow: Mediterranean Sea application,' Ocean Engineering, vol. 220, Art. no. 108435, 2021.
[3] Y. Li et al., 'Oil spill detection with multiscale conditional adversarial networks with small-data training,' Remote Sensing, vol. 13, no. 12, Art. no. 2378, 2021.
[4] Y. Chen and Z. Wang, 'Marine oil spill detection from SAR images based on Attention U-Net model using polarimetric and wind speed information,' IJERPH, vol. 19, no. 19, Art. no. 12315, 2022.
[5] Y. Li et al., 'An adversarial learning approach to forecasted wind field correction with an application to oil spill drift prediction,' IJAEOG, vol. 112, Art. no. 102924, 2022.
[6] A. S. Dhavalikar and P. C. Choudhari, 'Prediction of oil spill trajectory on the ocean surface using mathematical modeling,' IEEE JSTARS, vol. 15, 2022.
[7] L. F. Tessarolo et al., 'A surface Lagrangian algorithm applied to the 2019 South Atlantic oil spill,' Ocean Engineering, vol. 268, Art. no. 113505, 2023.
[8] F. Chen et al., 'DGNet: Distribution guided efficient learning for oil spill image segmentation,' IEEE TGRS, vol. 61, 2023.
[9] C. Li et al., 'A self-evolving deep learning algorithm for automatic oil spill detection in Sentinel-1 SAR images,' Remote Sensing of Environment, vol. 299, Art. no. 113872, 2023.
[10] P. Cervantes-Hernández et al., 'Combined use of SAR images and numerical simulations to identify source and trajectories of oil spills,' MPB, vol. 199, Art. no. 115981, 2024.
[11] S. El Mohtar et al., 'Iterative data-driven construction of surrogates for efficient Bayesian identification of oil spill source parameters,' Computational Geosciences, 2024.
[12] T. V. La et al., 'Monitoring of spatio-temporal variations of oil slicks via the collocation of multi-source satellite images,' Remote Sensing, vol. 16, no. 16, Art. no. 3110, 2024.

## Slide 15
EVALUATION EVIDENCE
11. Geotagged Photo Verification
📷 [Attach Geotagged Photo Taken During Review 2 Presentation]
Instructions for Team: 1. Capture presentation photo in classroom / lab using GPS/Geotag camera app. 2. Ensure Latitude, Longitude, Date, and Timestamp are stamped on photo. 3. Replace this placeholder container with your actual captured photo.

## Slide 16
SOURCE CODE DELIVERABLES
12. Code Implementation & Execution Links
🔗 Google Colab & Repository Implementation Links
• Google Colab Pipeline Link: [Insert Google Colab Shared Link Here]
• Local Workspace Repository: C:\Users\Jayalakshmi\oil_spill\
• Data Preprocessing Pipeline: data_preprocessing.py
• Novel Deep Learning Architecture: model_architecture.py
• Benchmark Evaluation Engine: train_and_benchmark.py
• Generated Evaluation Deliverables: results\ (Metrics CSV, PNG charts, Markdown reports)

## Slide 17
THANK YOU
Questions & Feedback